## Slide 1: Principles of Cyber-Physical Systems Chapter 1: Introduction
Instructor: Rajeev Alur alur@cis.upenn.edu

## Slide 2: Embedded Software Systems Everywhere!
Software Inside
Principles of Cyber-Physical Systems: Introduction

## Slide 3: From Desktops to Cyber-Physical Systems
Traditional computers: Stand-alone device running software applications (e.g. data processing)
Traditional controllers: Devices interacting with physical world via sensors and actuators (e.g. thermostat)
Embedded Systems
  Special-purpose system with integrated microcontroller/software
  Cameras, watches, washing machines…
Principles of Cyber-Physical Systems: Introduction

## Slide 4: Cyber-Physical Systems
Control
Monitor and influence
physical world
Computation
Process information
to make decisions
Communication
Exchange data
to collaborate
Principles of Cyber-Physical Systems: Introduction

## Slide 5: Cyber-Physical Systems
Driverless Cars
Medical devices
Coordinating robots
Principles of Cyber-Physical Systems: Introduction

## Slide 6: Design of Cyber-Physical Systems
Systems that integrate control, computation, and communication can do
Cool things,
And useful things…
Lots of promise and potential: medicine, transportation, energy, …
So what’s the challenge?
Principles of Cyber-Physical Systems: Introduction

## Slide 7: Ariane 5 Explosion
“It took the European Space Agency 10 years and $7 billion to produce Ariane 5. All it took to explode that rocket less than a minute into its maiden voyage last June, scattering fiery rubble across the mangrove swamps of French Guiana, was a small computer program trying to stuff a 64-bit number into a 16-bit space”
A bug and a crash, J. Gleick, New York Times, Dec 1996
Principles of Cyber-Physical Systems: Introduction

## Slide 8: Prius Brake Problems Blamed on Software Glitches
“Toyota officials described the problem as a "disconnect" in the vehicle's complex anti-lock brake system (ABS) that causes less than a one-second lag. With the delay, a vehicle going 60 mph will have traveled nearly another 90 feet before the brakes begin to take hold”
CNN Feb 4, 2010
Principles of Cyber-Physical Systems: Introduction

## Slide 9: Software: The Achilles’ Heel
Software everywhere means bugs everywhere
  2002 study by NIST:
  Software bugs cost US economy $60 billion annually (0.6% of GDP)
Lack of trust in software as technology barrier
  Would you use an autonomous software-controlled round-the-clock monitoring and drug-delivery device?
Grand challenge for computer science:
Technology for designing reliable cyber-physical systems
Principles of Cyber-Physical Systems: Introduction

## Slide 10: Let’s Design a Cruise Controller
What’s the goal of a cruise controller?
Automatically adjust the speed of the car so that it matches the speed desired by the driver
Principles of Cyber-Physical Systems: Introduction

## Slide 11: Block Diagrams of High-Level Design
CruiseController
How does this component interact with the rest of the world ?
Principles of Cyber-Physical Systems: Introduction

## Slide 12: Interfaces for Components: Inputs and Outputs
CruiseController
Driver interacts with the system using 4 buttons:
Cruise button to turn the cruise on or off
Pause button to suspend/restart its operation
Inc and Dec buttons to increment or decrement desired speed
cruise
pause
inc/dec
Driver
Principles of Cyber-Physical Systems: Introduction

## Slide 13: Interfaces for Components: Inputs and Outputs
CruiseController
What other information does the cruise-controller need ?
And who supplies it?
Tachometer
speed
cruise
pause
inc/dec
Driver
Principles of Cyber-Physical Systems: Introduction

## Slide 14: Interfaces for Components: Inputs and Outputs
What should be the outputs of the cruisecontroller?
And who needs these outputs?
CruiseController
Tachometer
speed
cruise
pause
inc/dec
Driver
Principles of Cyber-Physical Systems: Introduction

## Slide 15
CruiseController
Driver
cruise
pause
inc/dec
Tachometer
speed
Display
speed
DesiredSpeed
Throttle
Force
Principles of Cyber-Physical Systems: Introduction

## Slide 16: Compositional Design
CruiseController
cruise
pause
inc/dec
speed
speed
DesiredSpeed
Force
How to break up the computation of the cruise controller into subtasks?
Principles of Cyber-Physical Systems: Introduction

## Slide 17: Decomposing the Cruise Controller
cruise
pause
inc/dec
speed
speed
DesiredSpeed
Force
SetSpeed
ControlSpeed
Principles of Cyber-Physical Systems: Introduction

## Slide 18: Designing SetSpeed Component
cruise
pause
inc/dec
speed
DesiredSpeed
SetSpeed
Goal: Compute the desired cruising speed in response to
the commands from the driver
Principles of Cyber-Physical Systems: Introduction

## Slide 19: Designing SetSpeed: State Machines
OFF
ON
PAUSED
cruise: r := speed
cruise
pause
pause
pause, inc, dec
cruise
inc: r := r+1
dec: r := r-1
DesiredSpeed corresponds to the variable r
inc, dec
Principles of Cyber-Physical Systems: Introduction

## Slide 20: Designing ControlSpeed Component
DesiredSpeed
speed
Force
ControlSpeed
Goal: Determine the force to be applied to throttle so that speed becomes equal to DesiredSpeed
Principles of Cyber-Physical Systems: Introduction

## Slide 21: Capturing Requirements
DesiredSpeed
speed
Force
ControlSpeed
Requirements: Mathematically precise description of what a system is supposed to do.
Writing requirements is key to ensuring reliability of systems
Requirement 1: Actual speed eventually converges to desired speed
Requirement 2: Speed of the car stays “stable”
Principles of Cyber-Physical Systems: Introduction

## Slide 22: A bit of Physics: Modeling a car
Velocity v
Force F
Friction k v
Newton’s law of motion gives
F – kv – mg sin q = m a
Angle q
Weight mg
Principles of Cyber-Physical Systems: Introduction

## Slide 23: ControlSpeed Component
DesiredSpeed r
Force F
ControlSpeed
Control Theory: Mathematical techniques to compute force (F) as a function of velocity (v) and desired speed (r)
Car
Angle q of the road with horizontal (disturbance)
Velocity v
F – kv – mg sin q = m a
F = KP ( v – r)
Principles of Cyber-Physical Systems: Introduction

## Slide 24: Does our controller work ?
r
Force F
ControlSpeed
Car
q
Velocity v
F – kv – mg sin q = m a
F = KP ( v – r)
Verification Tools: Allow you to check if system model indeed works as expected, that is, satisfies requirements
Principles of Cyber-Physical Systems: Introduction

## Slide 25: Model-based design != Coding
Design using high-level block diagrams and state machines gets automatically compiled into low-level code !
Models not only of system being designed, but also of its environment
Principles of Cyber-Physical Systems: Introduction

## Slide 26: Verification != Simulation/Testing
Model/Program
Requirement
yes/proof
no/bug
Verifier
Program testing can be used to show the presence
of bugs, but never their absence!
Edsger W. Dijkstra
Principles of Cyber-Physical Systems: Introduction

## Slide 27: Formal Verification
Model/Program
Requirement
yes/proof
no/bug
Verifier
Goal: Establish that model satisfies requirements under all possible scenarios
First challenge: Need formal definitions of “model” and “requirement” to make the problem mathematically precise
Second challenge: Need verification techniques and tools
Principles of Cyber-Physical Systems: Introduction

## Slide 28: Course Topics
Goal: Introduction to principles of design, specification, analysis and implementation of CPS
Disciplines
  Model-based design
  Concurrency theory
  Distributed algorithms
  Formal specification
  Verification techniques and tools
  Control theory
  Real-time systems
  Hybrid systems
Emphasis on mathematical concepts
Principles of Cyber-Physical Systems: Introduction

## Slide 29: Theme 1: Formal Models
Mathematical abstractions to describe system designs
Modeling formalisms
  Synchronous models (Chapter 2)
  Asynchronous models (Chapter 4)
  Continuous-time dynamical systems (Chapter 5)
  Timed models (Chapter 7)
  Hybrid systems (Chapter 9)
Modeling concepts
  Syntax vs semantics
  Composition
  Input/output interfaces
  Nondeterminism, fairness, …
Principles of Cyber-Physical Systems: Introduction

## Slide 30: Theme 2: Specification and Analysis
Formal techniques to ensure correctness at design time
Requirements
  Safety (invariants, monitors)
  Liveness (temporal logic, automata over infinite sequences)
  Stability
  Schedulability
Analysis techniques
  Deductive: Inductive invariants and ranking functions
  Enumerative and symbolic search for state-space exploration
  Model checking
  Linear-algebra-based analysis of dynamical systems
  Verification of timed and hybrid systems
Principles of Cyber-Physical Systems: Introduction

## Slide 31: Theme 3: Model-based Design
Design and analysis of illustrative computing problems
Design methodology
  Structured modeling (bottom-up, top-down)
  Requirements-based design and design-space exploration
Case studies
  Distributed coordination: mutual exclusion, consensus, leader election
  Communication: Reliable transmission, synchronization
  Control design: PID, cruise controller
  CPS: Pacemaker, obstacle avoidance for robots, multi-hop control network
Principles of Cyber-Physical Systems: Introduction