## Slide 1: Modeling Plants, Sensors & Actuators
Ramesh S

## Slide 2: Model based development
Plant
Controller
Environment
Plant Model
Controller Model
Environment Model
Link Model
Link Model
Model
Real System

## Slide 3: Modeling Plants
Involves identification of physical variables governing the plant behavior
  Plant variables are continuous or real values variables
model how these plant variables vary over time and respond to control inputs and environmental changes
Algebraic and/or Differential Equations over the plant variables
Example: For thermostat controller, plant variable include room temperature, humidity level
T > tmax
T < tmin
on
off
T’ = K1
T’ = K2

## Slide 4: Why model plants?
To design and validate controllers
Modeling involves right level of abstraction
  Physical systems are quite complex and often not necessary for modeling all aspects of physical phenomenon
  Especially for control system design and validation
Models are used for the design of physical plants themselves but these tend to be quite elaborate
  Not needed for control system design and validation
Physical models often measured by the degrees of freedom that they possess
  Higher the degrees of freedom more complex the model
  3-DoF models and 6-DoF models in aircraft and automotive design

## Slide 5: Vehicle Models
Vehicles are multi-body systems - complex interconnection of rigid and flexible bodies
  When engine produces thrust various tensile and shear forces operate to make the vehicle move
Faithful modeling requires multi-body simulation
  Simple models use lateral and longitudinal velocity, accelerations, position are some of the important variables,
  More complex modeling involves tire pressure, surface friction are also variables for complex modeling
Kinematic models - algebraic equations involving velocity, acceleration and position
  Low Speed Maneuvers, No/Little lateral motion, no surface slip assumed
Dynamic Models – differential equations considering forces
  High speed Manuevers, Lane Change and Obstacle avoidance controllers

## Slide 6: Commercial Vehicle Models
Elaborate commercial vehicle models available and used in practice
  MSC Adams, ANSYS Motion
  Modeling tires and tire forces on roads are the most complex
For Design & Development of Vehicle Controls
  Models the behavior of vehicles for different road conditions under different driver inputs like throttle, brake and steering
  e.g., Carsim (AI), CarMaker (IPG Automotive)
  Extensively used by several automotive companies

## Slide 7: Environment Modeling
Besides plants, sensors/actuators, environment objects also requires modeling
In the case of automated driving systems, 3d environment objects like roads, road-side objects like signals, lane markers, building, pedestrians , intersections are all to be modeled.
Powerful simulation engines are being used in creating scenes and scenarios
  Applied Intuition, dSpace, ANSYS, Open source tools (Carla)

## Slide 8: Environment Modeling
Environment plays a crucial role in most embedded systems
Environment includes elements external to, (partially) observable but not directly controllable by the controller
  Contrast with the plant
They may involve physical and human element
In the case of automotive systems, the environment is the 3D object world
  Roads, Road Signals, Other vehicles, Pedestrians (VRUs), Trees, side walks, lanes, buildings, etc.
  Weather and weather-related objects, lighting conditions,
Modeling involves identification and digital representation of appropriate aspects of the environmental elements
  Focus on aspects that concern the controller
  Focus on aspects that impact the sensors (e.g., surface reflecivity)
These include
  Road geometry, Road physics
  Road object physics (shape, surface reflectivity, position, velocity and acceleration)
  Weather - Rain/snow (low, medium & heavy),
  Lighting (dark, bright, nominal)

## Slide 9: Scenes and Scenarios
Digital representation of environment
A scene has
  background (sky, paved and unpaved areas, sidewalks, etc.)
  Static objects (e.g., signboards, buildings, trees, bushes, etc.
  Dynamic actors (ego vehicle, other vehicles, signals, pedestrians, etc.)
Each dynamic actors is associated with a behavior
  Vehicles and pedestrians have trajectories
  Signals periodically change
A scenario is timed sequence of scenes
  Background and static objects change from one scene to another depending upon the workd
  Dynamic actor change as per their behaviors
Scenario description languages
  Open Scenario 2.0
Scenes and scenarios
  Are rendered as photo-realistic images in gaming engines (Unity, Unreal)
    Enabled by Nvidia RTF technology
  Edited to create or revise new scenes and scenarios (Mathworks Roadrunner)

## Slide 10: Real to Virtual
Several companies are involved in creating digital representation of all the roads and road-side static objects
Open Street map

## Slide 11: Radar Scene Emulator

## Slide 12: Sensing: Basic Concepts
Ramesh S

## Slide 13: Sensors
Sensors and sensor circuitry are fundamental to embedded systems
Involve transduction of external physical parameters to electrical parameters
  Physical parameters are temperature, pressure, acceleration, concentration, etc
  Electrical Parameters are: Voltage, Current, Resistance, Capacitance
This is a classical definition applicable to small restricted class of embedded devices
A very general definition required for modern AI based applications like self driving cars, large scale IoT devices
  Eg., collision avoidance system need to sense `collision situation’, Conference room adjust the lighting and sound `sensing’ (inferring) the number and spread of attendees
Philosophy and Psychology have very general definition
  Sensing involves creating a `consistent model’ of the external phenomenon/envn.

## Slide 14: Sensors
Sensor
r(t)
Plant
s(t)

## Slide 15: Sensor/Actuator Modeling
A variety of sensors used in embedded systems
  Temperature, pressure and touch sensors, gyroscopes
  Wheel speed sensors, Accelerometers, GPS devices
  Cameras, Radars, Lidars
Sensor modeling important aspect in MBD
Simple sensors are transducers that convert some physical parameters into digital variables
The simplest model of an ideal sensor is an affine function:
  S = f(X) = aX + b, a is called sensitivity and b is the bias
  X, is the physical parameter and S is the corresponding digital signal or value
In reality, there will be range for a sensor
Other aspects to be considered are noises and distortions
A common way of modeling simple sensors is as a transfer functions

## Slide 16: Sensor Challenges
Physical parameter varying over time and the challenge of sensors is to follow and capture accurately the changes
  s(t) = F(r(t)), for all time points, t
What is an ideal sensor?
  s(t) = K * r(t), for all t
  Constant gain sensor
Also, ideally K is very high so that small changes in input are discernible – high sensitivity
Why is this ideal?
  Inverse function is easy to construct
  Why do you need to construct inverse function?

## Slide 17: Sensor Characteristics
Static Characteristics
  Properties of the sensors in the steady state after all transient effects are settled
  Accuracy
  Resolution
  Precision
  Sensitivity
  Linearity
  Hysteresis
Dynamic Characteristics
  Sensor properties under changes in physical parameters
    Zero, first and second order systems

## Slide 18: Accuracy, Resolution, Precision
Accuracy of a sensor determines the error in measurement
  Absolute Error, Relative error = abs. error/ true value
Resolution is the smallest change in the parameter that are detectable or measurable by the sensor
A precise sensor is one that measures/senses the same value when the actual values are the same
Sensitivity is a measure of the slope of the I/O curve
  I/O curve is also called calibration curve
Linearity is a measure of closeness of the curve to a straight line
Monotonicity
Hysteresis is measure of the difference in measured values of the parameter value reached from

## Slide 19: Dynamic Characteristics
Static characteristics of a sensor describes the behavior under nonvarying inputs
Dynamic behavior describes the sensor outputs under changing inputs
The inputs can change in a variety of ways
  Impulse, Step, Linear, Sinusoidal, Mixed With High and Low Frequency Noise

## Slide 20: Sensor Response
How should a sensor response be for varying inputs
Ideally, sensor should transduce faithfully and instantaneously the intended changes in input
  Constant gain sensor for all frequency range – infinite bandwidth
  Difficult to achieve in practice
Real sensors will have some storage element
  Eg., Typical accelerometers will have a mass spring arrangement
  Temperature sensors will have heating element that has associated delay
Real sensors have ranges of operations
  Linear behavior in some range
  Non-linear behavior, saturation outside the range
Real sensors have finite bandwidth

## Slide 21: Transfer Function
Dynamic Behavior of a sensor is characterized by a transfer function
Inputs and outputs are related, in general, by differential equations
The order of the differential equation determines the order of the sensor
  Zero order sensor: Potentiometer measuring linear and rotary displacements
  First order sensor: Thermocouple measuring temperature changes
  Second order sensor: Accelerometer

## Slide 22: Dynamic Model of Sensors
The dynamic response of a sensor often defined by a linear differential equations
Using Laplace transforms this can be converted into algebraic equations:
Transfer function is then
Poles and Zeros decide the behavior of the sensor

## Slide 23: Relating Poles and Sensor Behaviors

## Slide 24: First Order Sensor
Transfer Function: G(s) =
Step Response:
  A – step size
  k is static gain
  τ is Time constant
Ramp Response

## Slide 25: First Order Sensor Response

## Slide 26: Second Order Transfer Function
Transfer function

## Slide 27: Second-order Step Response

## Slide 28: Second-Order Response

## Slide 29: Other Issues with Sensors
Sensor power might be limited to drive the controller or load
Sensor has an output impedance
For voltage sensors, the output impedance need to be very small
For current sensors, the output impedance need to be very high

## Slide 30: Sensor Errors
Systematic Errors
  Inherent transduction process error
  Drifting due to age
  Transmission Errors – attenuation
  Loading Error – measurement changes the value
  Saturation, Non linearities
Random Errors
  Noise is everywhere
  White Noise (Gaussian Noise)
  Environmental Interference – 60Hz hum
  SNR >> 1
Digital Inputs too subject to noise
  Debouncer circuits

## Slide 31: Sensor Circuitry
Elaborate interfaces often required for sensors in view of the above issues
The interface circuitry includes
  High input impedance devices (voltage sensors)
  High Gain Amplifiers
  Buffers
  Filters
Many microcontrollers (e.g., PSoC4) enables developing sensor specific interfaces by providing a number of analog blocks
  OpAmps – Operational Amplifiers

## Slide 32: OpAmps
Schematic Symbol
Very High Gain Differential Amplifier
Active Circuit with a power supply
I/O with respect to a ground
Voltage Amplifier
+V, -V external supply
+
+
-
+V
Output
Inverting Input
Non Inverting
Input
- V

## Slide 33: What is an amplifier?
Rs – Source Resistance
RL – Load Resistance
Vs – Source Voltage
Vo – Output Voltage
Vo = Gain * Vs
Amplifier
Rs
Vs
Vo
RL

## Slide 34: Amplifier – Equivalent Circuit
Rin – Input Resistance
Rout – output Resistance
Vin – Voltage across Rin input to the amplifier
  Fraction of Vs
A – Voltage Gain
Rs
Vs
VL
Rin
Vin
RL
A
A x Vin
+
-
Rout

## Slide 35: Ideal OpAmp
Input Resistance Rin is infinity
Output Resistance Rout is zero
Amplifier Gain A is infinity
A – Open loop gain
+
-
+
-
Rout
Vn
Vp
A*Vd
Rin
- V
+ V

## Slide 36: Negative Feedback
Connect the output of the Opamp to the inverting input
Input is connected to the inverting input
What is the relation between Vs and Vo ?
What is the input voltage to OpAmp? Vp – Vn
-
+
Vs
Rs
Rf
Vo
Vn
Vp

## Slide 37: Analysing Ideal OpAmp
The inverting amplifier is equivalent to the below figure. How?
Simple circuit analysis will show that
  Vout = - [Rf/(Rs)] * Vs
Output is inverted in sign compared to input
  Inverting amplifier
Closed loop gain independent of the gain of OpAmp!
  Chosen by adjusting the values of feedback resistance
Vs
Rs
Rf
Vn
AoVin
Vout
Vp

## Slide 38: Important Properties of Ideal OpAmp
With Negative feedback
What is the input voltage applied to the OpAmp?
The Input Voltage Constraint:
  Vp = Vn
  It is virtual short circuit
What is the current flowing in/out of OpAmp?
The input current constraint:
  Ip = In = 0
  It is a virtual open circuit

## Slide 39: Versatility of OpAmp
OpAmp appears to be a paradoxical circuit
But a very powerful and versatile component
Important building block in Analog Circuits
They can be used to build a variety of functionality
Inverting and noninverting amplifiers, Voltage follower or buffer
Converters, Filters, Comparators
Arithmetic and Logical Operations – Hybrid Computers

## Slide 40: More Complex Sensors
Elaborate techniques required for modeling sensors like Cameras and radars
Cameras are sensors that convert 3D physical world scenes into pixel values
A model needs to do the same: inputs 3D objects and outputs pixel values
There are two main approaches used for modeling cameras
  Rastering and Ray Tracing
Rastering involves computing projections and less expensive and accurate compared to ray tracing
Ray tracing traces different rays of light going from source to the camera
Effects of camera lenses need to be modeled