## Slide 1: SCENARIO-BASED TESTING (SBT) OF EMBEDDED SYSTEMS
RAMESH S. & ARUN A.
CS 522 – EMBEDDED SYSTEMS | IIT-G
OCTOBER 26, 2023

## Slide 2
SCENE
A scene describes a snapshot of the environment including the scenery and dynamic elements, as well as all actors’ and observers’ self-representations, and the relationships among those entities.

## Slide 3
SITUATION
A situation is the entirety of circumstances, which are to be considered for the selection of an appropriate behavior pattern at a particular point of time. It entails all relevant conditions, options and determinants for behavior.

## Slide 4
SCENARIO
A scenario is a temporal sequence of scenes
A scene is a snapshot of the environment including the scenery and movable objects, as well as actors’ and observers’ self-representations, and the relationship among those entities
Scenario abstractions:
Abstraction Level | Description | Example
Functional | A qualitative verbal description | The ego car drives on a straight road at a high speed
Logical | Set of parameter ranges and potentially with distributions | The ego car drives at a speed between 10 m/s and 20 m/s
Concrete | A set of exact parameter values | The ego car drives at 15 m/s

## Slide 5
SCENARIO

## Slide 6: SBT IN UNMANNED AERIAL VEHICLES (UAVs)

## Slide 7
UAVs - EXEMPLARY OPERATING CONDITIONS

## Slide 8
LOGICAL VS CONCRETE SCENARIO

## Slide 9
FORMAL DESCRIPTION

## Slide 10
SIMULATION-BASED OPTIMAL TEST GENERATION

## Slide 11
SIMULATION-BASED OPTIMAL TEST GENERATION
(I) – Logical scenario in which we like to evaluate UAV behavior
(II) – Optimization algorithm for “good” test cases generation
  Fitness function : encodes safe behavior in a concrete scenario
      : minimum distance that the UAV keeps to obstacles at time in a concrete scenario (cs)
      : specified safe distance

## Slide 12
SIMULATION-BASED OPTIMAL TEST GENERATION
(III) – build concrete scenario in the simulation environment
(IV), (V), (VI) – Instantiate concrete scenario parameter values, execute the concrete scenario, and log the simulation data
(VII) – Compute the fitness values of each concrete scenario and generate further concrete scenarios

## Slide 13: SBT IN AUTOMATED DRIVING SYSTEMS (ADS)

## Slide 14
AUTOMATED DRIVING SYSTEM (ADS)
Consumes real-time sensor data
  Cameras, RADAR, LiDAR, GPS, …
Localization using HD Maps
Perception: Obstacles, traffic signs, …
Prediction: trajectories of perceived objects
Planning: trajectories for the Ego vehicle
Control: Control commands (steer, brake/throttle)

## Slide 15
SAFETY ASSESSMENT
Assessment across entire operational design domain (ODD) of the system
  ODD: Operating conditions under which a given ADS is designed to function
Component-level assessment
  Individual components
  E.g.: Object detection part of the perception component
System-level assessment
  Functionalities backed by multiple components and interaction among them
  E.g.: reach a destination without any collisions navigating through intersections
Two assessment approaches are complementary

## Slide 16
CONVENTIONAL TESTING VS SBT
Generic testing
  Ego vehicle drives on public roads with uncontrollable and unpredictable traffic scenarios
  Inefficient in covering rare events/challenging scenarios
Scenario-based testing
  Testing challenging scenarios
  Gain confidence on functionality and safety

## Slide 17
LAYERED SCENARIO MODEL

## Slide 18
SCENARIO-BASED TESTING WORKFLOW
Example: ACC functionality in highway environments
Static config. C: map, background object behavior; Searchable space D
Test objective: find scenarios causing Ego vehicle collision

## Slide 19
SCENARIO PARAMETERS
Layer 1
Road layout parameters: curvature, ramp, surface friction, number of lanes
Layer 4
Object behaviors: control at initialization, control for activated behavior, and control at every step
Layer 5
Environmental conditions like weather and lighting
Rain, fog, snow, cloud, wind intensity, wetness, snow, sun angle, light intensity

## Slide 20
TESTING OBJECTIVES
SPECIAL SCENARIOS SEARCH
Goal is to find scenarios satisfying specific properties efficiently
Finding qualified scenarios (more)
Finding scenarios with best values (severe)
Quickly finding the first qualified scenario (first)
PERFORMANCE EVALUATION
Collision rate
Task failure rate
Critical rate
Critical value
Critical boundary

## Slide 21
ALGORITHMS FOR SCENARIO SEARCH
NON-ADAPTIVE
  Does not access the information from the environment or system
SIMULATION-BASED ADAPTIVE
  Generates a batch of test functions at a time
  Passes test functions to scenario execution module to run
  Leverages feedback to generate next batch
  E.g.: Evolutionary algorithms, Simulated annealing, …
STEP-BASED ADAPTIVE
  Generates one test function
  Constantly get feedback from the environment to generate next test function
  E.g.: Reinforcement learning

## Slide 22
DATA-DRIVEN SCENARIO GENERATION

## Slide 23
(I) SOURCE DATA COLLECTION
Natural Driving Data (NDD)
  Traffic data collected in the physical world
  Sensors mounted on the vehicles or physical infrastructure
Accident Data
  Several databases document crash/near-crash scenarios
Virtual Data
  Data from high-fidelity 3D simulators

## Slide 24
(II) SCENARIO IDENTIFICATION
Source data mining
Filter out unnecessary/uninteresting scenario data
Reduce feature dimensions
Identify known and unknown scenarios in source data

## Slide 25
(III) SCENARIO GENERATION
Coverage and Criticality of scenarios are crucial
Methods:
  Random sampling
  Combinatorial testing
  Mutation testing
  Reinforcement learning

## Slide 26
(IV) SCENARIO EVALUATION
Criticality measure for scenarios
Trajectory: calculated using trajectories of all traffic participants
Maneuver: measure the difficulty of avoiding an accident
Energy: measure severity of crash (kinematic energy released during crash)
Uncertainty: more uncertainties the better (e.g.: road friction, velocity variance of vehicles)
Combination: integrates several metrics; multi-dimensional analysis

## Slide 27: ADS SIMULATION

## Slide 28
ADS TESTING
Rigorous testing essential to
  Ensure robust functionality and safety
  Widespread adoption
Real World
  Constructed in the real world (public or closed-course)
  High fidelity
  Uncontrollable and unpredictable
  Expensive, non-scalable, dangerous in certain scenarios
Virtual
  Complement traditional methods
  Repeatability and reproducibility
  Scalable
  Cost-effective

## Slide 29
X-in-the-Loop (XIL) TESTING
Model-in-the-Loop (MIL)
  Simulation on a general computing system
  Software model + plant model
Software-in-the-Loop (SIL)
  Simulation using compiled code
  Software + plant model
Hardware-in-the-Loop (HIL)
  Hybrid solution combining simulated models with real hardware components
  Software + plant model + physical embedded hardware
Virtual Hardware-in-the-Loop (VHIL)
  Software + plant model + virtual embedded hardware

## Slide 30
ADS SIMULATION CONTENT
Static Environment Simulation
Dynamic Environment and Behavior Simulation
Traffic Flow Simulation
Sensor Simulation
Vehicle Dynamics Simulation

## Slide 31
STATIC ENVIRONMENT SIMULATION
Composed of 3D models of
  Terrains
  Road network structure
  Road type
  Buildings
  Vegetation
  Traffic sign

## Slide 32
DYNAMIC ENVIRONMENT & BEHAVIOR SIMULATION
Microscopic
  Vehicles
  Pedestrians
  Weather conditions
  Lighting
Macroscopic – traffic flow
Interaction of traffic participants with the Ego vehicle (vehicle-under-test)

## Slide 33
DYNAMIC ENVIRONMENT & BEHAVIOR SIMULATION
COLLISION MODELS
Low-fidelity
  Using relative velocity and heading angle to directly estimate the damage of the collision
Medium-fidelity
  Using involved agent’s kinematic to determine acceleration and classify the damage
High-fidelity
  Using FEM to precisely compute forces exerted during the collision

## Slide 34
TRAFFIC FLOW SIMULATION
Studies the behavioral interaction between each vehicle on the road and the Ego vehicle
At macro level, continuous compressible fluid composed of a large number of vehicles, focusing on aggregated variables such as average speed and average density

## Slide 35
SENSOR SIMULATION
Enable ADS to perceive its environment, identify and classify participants and the behavior
Types:
  Camera
  RADAR (short and long range)
  LiDAR
Positioning and properties influence field-of-view

## Slide 36
SENSOR SIMULATION
FIDELITY
Low-fidelity
  Black-box models or object list (retrieved directly from simulation environment)
  Doesn’t cover statistical aspects (false positives/negatives) related to perception
  Cover basic aspects such as field of view (FOV) and occlusions
Medium-fidelity
  Grey-box
  Model effect of traffic objects’ shape and texture, atmospheric degradation
High-fidelity
  White-box or physics-based
  Ray tracing/rasterization to render 3D simulation environment

## Slide 37
VEHICLE DYNAMICS SIMULATION
Reflect physical properties of vehicle
  Degrees of Freedom (DoF)
  Motion control
  Center of mass and inertial characteristics
  Suspension
  Braking
  Acceleration/Deceleration
Configure model parameters based on test objectives

## Slide 38
VEHICLE DYNAMICS SIMULATION
FIDELITY
Low-fidelity
  Point-mass or kinematic models
  Used for controller synthesis or microscopic traffic studies
Medium-fidelity
  Chassis models with linear or non-linear tires
  Used for synthesis of model predictive controller
High-fidelity
  Multi-body models, including suspensions geometry, chassis compliance, engine mounting stiffness and damping characteristics, driveline dynamics, tire contact points, …

## Slide 39
SIMULATION PLATFORMS