## Slide 1: Real-Time Operating System (RTOS) S. Ramesh

## Slide 2: Operating Systems
What is an OS?
  Provides an abstraction of the raw computing HW resources (CPU, Memory, Disk, etc.)
    Ease of application development
    Abstract & Efficient utilization of resources
    Reuse of well-proven standard functions
OS structured as a layered architecture
  core or kernel performing basic function
  a series of outer shells: I/O, user functions

## Slide 3: Abstract Architecture
Kernel
File and Disk I/Ot
Hardware
User Interface
Applications

## Slide 4: Concrete Architecture -Automotive

## Slide 5: Layered Architecture
Each layer uses the services of lower layer and provides service to the upper layer
Service are in the form of function calls
Kernel provides basic functions
  task management, scheduling, communication
  Timer services
  External I/O management
System calls and APIs
RTOS usually has only the kernel

## Slide 6: Kernel Functions
Interrupt Servicing & Scheduling
Timer Service & Scheduling
Task, Time and other I/O services5
External Interrupts
Clock Interrupts
System Calls

## Slide 7: Task Management
Task is a sequential computation
Time or event triggered
Task may be running or wait for I/O or other tasks
Tasks may be created or destroyed
Task behavior realized by the OS or RTOS

## Slide 8: Task State Machine (Simplified)
Ready
Executing
Waiting/Suspended

## Slide 9: Managing the tasks
A task when it enters the system is either in waiting or ready state
It is in ready state when it is ready for execution but some other task is currently executing
It can go to executing state only from ready state
An executing task can be preempted by hi-priority tasks and may enter the ready state
An executing task goes to waiting state when an input or resource required for execution
Component of RTOS which manages the tasks is called the scheduler

## Slide 10: Preemption
When is a task preempted?
  When it requires a new input/event?
  When a hi-priority task is ready
  When a shared resource is not ready
    Printers, network interface buffers etc.
  When a time slice for a task expires
    Round robin scheduling of tasks
Preemption is often asynchronous and one has to assume the worst can happen
  Just when a memory read has happened
Saving grace is that it happens in instruction boundaries
  What instructions? High Level instructions?
  No machine level instructions
Controlled preemption is essential to predict the results of computation

## Slide 11: Context-switching
What happens when an executing task T1 is pre-empted by another task T2
The state of T1 needs to be saved so that when T1 is resumed later, it resumes from where it left
What decides the state of a task
  Its control point
  All the register values
  The stack
What about memory?
  Memory is often shared among the tasks
  It could be changed by new running tasks
  It is used for communication between tasks
  So no memory copy is made
  The result is that memory would contain arbitrary value on resumption

## Slide 12: Task Control Block (TCB)
Stores the entire state of a task
.
.
TID
SAVED_TASK_STATE
Resource 1 (signals)
Resource 2 (events)
Resource 3 (shared memory)
System Variables

## Slide 13: Task Timing Diagrams
T1
T3
T2
T4
Response Time of T1
Preemption
Resumption