## Slide 1: RTOS Other Features
S. Ramesh

## Slide 2: Time Services
Very basic for Real-Time Systems
Different activities are carried out based upon the elapse of time
  Periodic invocation of tasks
  Watchdogs and Time-outs
  Delays
Hardware Clock device
  To support such services
  One or more devices
  It has a counter, timer queue and an interrupt handler
  updated periodically by the clock pulse
  order of nanoseconds in modern HW

## Slide 3: SW or System Clock
Clock resolution available to applications is usually less than HW clock resolution
Kernel maintains a SW clock for each clock device
  This is what is available for applications
  Programs the HW clock to interrupt the kernel periodically
  Resolution is the period of the interrupts
  This can range from 100s of microseconds to 10s of milliseconds
SW clock resolution is a design parameter
  Higher the resolution more time kernel spends
Direct connection to HW clock is done for higher resolution – nanoseconds, by memory mapping HW clocks
But portability is lost

## Slide 4: Timers
Application tasks to have its own timers
Calling a create_timer function creates a timer and binds to a clock
Associated with each timer is the expiration time and a handler invoked when the timer expires
Timers can be periodic or one-shot
One-shot timers are Watchdog timers – standard in RT systems
    do . . . watching 20 milliseconds

## Slide 5: Timer Queues
RTOS maintains a queue of increasing expiration timer values
Handler routines are associated with each entry
With each clock interrupt, the queue is checked for expiration of an entry and the corresponding handler is inserted into the ready queue.
Tasks waiting on these timers would then go to the ready state
In time triggered systems, a timer can transfer the control to the scheduler
This periodic interrupt by the clock device decides the rate at which scheduling decisions are made, inputs are observed and outputs are generated

## Slide 6: Clock Resolution
Milli- and micro-second resolution can be done with timer queue based implementation
Finer resolution, of the order of nano seconds may be difficult due to the overhead
In some systems, the SW can directly access the HW timers
  Portability is an issue

## Slide 7: Resolution and Accuracy of SW Timers
More the frequency finer the resolution
TaskDelay(5)

## Slide 8: Variety of Communication Mechanisms
Semaphores, Message Queues, Mailbox, Pipes
Events
  Events are boolean flags like semaphores
  More than one task waiting for an event
  More than one event a task can wait
    Any event can trigger the task

## Slide 9: Characteristic Features RTOS
Clock and Timer support
Real-time priority levels – fixed priorities
Fast task preemption
Predictable and fast Interrupt latency
Support for Resource sharing
Support for RT scheduling
Memory management
  Virtual memory and paging introduces overheads and unpredictability
  Often avoided in many RT kernels

## Slide 10: Example RTOSs
PSOS (Wind River Systems)
VxWorks – Wind River Systems (Mars Pathfinder Project, PIP)
VRTX (Mentor Graphics)
QNX
RT-Linux
RT-POSIX
LynxOS
Non examples
  Unix, Windows