## Slide 1: Real-Time Scheduling S. Ramesh

## Slide 2: The Scheduler
It is one of the important components of RTOS
Efficient utilization of processor power among the tasks
Ensures timely execution of all the tasks
Which task to choose among the ready tasks is an important decision
Employs appropriate scheduler algorithm for taking this decision
Design and implementation of scheduler algorithm has been an active and rich area of research in Real-Time Systems

## Slide 3: The Scheduler
The scheduler maintains a queue of ready tasks
Schedulers are preemptive or non-preemptive
RTOS often employs preemptive scheduler
A preemptive scheduler preempts running tasks and brings in a new task for execution
The criteria for preemption is varied
  The running task waits for an event or resource
  A hi-priority task is ready
  The time slice for the running task is expired

## Slide 4: Important Notions
Valid Schedule: one task per processor at any time, after its arrival time and resource constraints met
Feasible schedule: A valid schedule in which tasks meet their deadlines
Scheduling Points: The Points at which the scheduler makes decisions
  Clock-driven or event-driven
  Scheduler is another task to be activated
Optimal scheduler: One that provides a feasible schedule if it exists

## Slide 5: Simple Process Model
The application consists of a fixed set of tasks
All tasks are periodic, with known periods
  Non zero phase possible
  Aperiodic (soft deadline) and Sporadic (hard deadline) Tasks
Tasks are independent of each other
All systems overheads, context-switching times ignored
Tasks have relative deadlines which are to be met in a schedule
  Usual assumption deadline same as period
All processes have known fixed worst-case execution time (WCET)
  Finding WCET of tasks is a challenging problem
Many of these assumptions pose problems in practice

## Slide 6: Scheduling Approaches
Two Broad Classifications:
  Clock-Driven Scheduling
    Table-driven Scheduling
    Cyclic Scheduling
  Event-Driven Scheduling
    Fixed Priority Scheduling
    Dynamic Priority scheduling
Clock-driven Scheduling
  Simplest, safe, highly predictable but restrictive
  Many small safety-critical embedded systems use this approach
Event-driven Scheduling
  Task release, task end, task wait events
  Rate-Monotonic Schedulers (RMS)
  Earliest Deadline First (EDF)

## Slide 7: Clock driven Scheduling
Example:
  Task set: period, wcet pairs
  T1: (4, 1), T2: (5, 1.8), T3: (20,1), T4: (20,2)
  Schedule these tasks so that their deadlines are met
    Usual assumption: deadline is at most the period
  Hyper-period is: 20 – The schedule can repeat every 20 units
T1
T3
T2
T1
T4
4
8
T1
T1
12
T1
T2
T2
T2
T1
16
20
2
1
9.8
6
13.8
18
0

## Slide 8: Table Driven Schedule
Task | Start Time (ms)
T1 | 0, 4, 9.8, 13.8,16
T2 | 2, 8, 12, 18
T3 | 1
T4 | 6
I | 3.8, 5, 10.8, 14.8, 17
Given the task periods, their start times are decided
The Schedule is pre-computed; the scheduler job is simple

## Slide 9: Table-driven Scheduling
Static and Simple
Easy to implement using timer interrupts
Highly deterministic and predictable
Aperiodic and sporadic tasks can be scheduled during Idle time
Simple systems are implemented using this scheme
Highly fragile – change in task set, wcet and release time, periods can not be tolerated

## Slide 10: Structured Cyclic Scheduling
Does not have a nice structure
Scheduling decisions are made at arbitrary points of time
A better cyclic schedule is one where scheduling decisions are made at periodic intervals of time, called Frames
No preemption of tasks within a frame
At the beginning of each frame, the scheduler can check jobs scheduled in the frame are released and is ready
Also whether there is any overrun so that corrective action can be taken
These put some constraints on the size of frames

## Slide 11: Frame Size
Frame size divides the period of at least one task
  This ensures that there is an integer number of frames per hyper-period
  Major cycle and integer number of frames (minor cycles)
Frame size is large enough to be greater than wcet of all tasks
Frame size is small enough so that between every release and deadline of each job, there is frame
Jobs may have to be sliced to meet these constraints

## Slide 12: Example revisited
For the tasks: T1: (4,1), T2: (5, 1.8), T3: (20,1), T4: (20,2)
The frame size is 2
T1
T3
T2
T1
T4
4
8
T1
T1
12
T1
T2
T2
T2
T1
16
20
2
1
10
6
14
18

## Slide 13: Cyclic Executives
The common way of implementing hard real-time systems
The cyclic executive divides the major cycle into frames
At every frame boundary, it checks whether the concerned tasks are ready/completed and necessary corrective or error handling taken care of
Set the timer to expire for the next minor cycle
The advantage is fully deterministic and predictable
Many classical safety-critical real time systems implemented using this scheme
Problems: Not robust, overruns and faults are difficult to handle

## Slide 14: Another Example
Task Period Computation Time
a 25 10
b 25 8
c 50 5
d 50 4
e 100 2

## Slide 15: Cyclic Executive
loop
wait_for_interrupt;
procedure_for_a; procedure_for_b; procedure_for_c;
wait_for_interrupt;
procedure_for_a; procedure_for_b; procedure_for_d;
procedure_for_e;
wait_for_interrupt;
procedure_for_a; procedure_for_b; procedure_for_c;
wait_for_interrupt;
procedure_for_a; procedure_for_b; procedure_for_d;
end loop;

## Slide 16: Time-line for Process Set
a
b
c
Interrupt
a
b
d
Interrupt
e
a
b
c
Interrupt
Interrupt

## Slide 17: Properties
No tasks exist at run-time; each minor cycle is just a sequence of procedure calls
The procedures share a common address space and can thus pass data between themselves.
  No need for semaphores and no associated problems
All “task” periods must be a multiple of the minor cycle time

## Slide 18: Problems with Cycle Executives
Sporadic activities are difficult (impossible!) to incorporate
The cyclic executive is difficult to construct and difficult to maintain — it is a NP-hard problem
Any “task” with a sizable computation time will need to be split into a fixed number of fixed sized procedures
  this spoils the structure of the code
More flexible scheduling methods are difficult to support
Determinism is not required, but predictability is

## Slide 19: Priority driven Scheduling
Does not leave any resource idle intentionally
They are event driven
Called greedy scheduling, list scheduling etc.
Tasks are assigned priorities and ready tasks are placed in a list or priority queue
Most real-time scheduling algorithms are priority-driven
  FIFO, LIFO, SETF, LETF, etc.
Priorities can be changed dynamically
  RR Scheduling is also in some sense a priority scheduling
Preemptive or nonpreemptive

## Slide 20: FPS and DPS
Event driven scheduling are of two kinds:
  Fixed Priority Scheduling (FPS)
  Dynamic Priority Scheduling (DPS)
In FPS, Each task has a fixed, static, priority which is computed pre-run-time
In DPS, tasks have no priorities but their instances (jobs) are
The scheduler executes the task instances as per their priorities
  At any time the current highest priority task is running

## Slide 21: Static Priority
Scheduling algorithm using static priority is easy to implement
Simply maintain a priority list
As and when new jobs (task instance) arrive, they find a place in the list
Task related events trigger the scheduler
scheduler picks the highest priority task for execution
Main problem: how do we assign static priorities so that tasks can be scheduled without violating their deadlines

## Slide 22: Simple Example
How do we schedule these two tasks?
How do we assign static priorities so that a priority based algorithm can be used
Suppose T2: (15,10) and T1: (5, 1)
T1
T2
p1
p2

## Slide 23: Rate Monotonic Priority Assignment
Each task is assigned a (unique) priority based on its period
  the shorter the period, the higher the priority
for two tasks Ti and Tj, Ti < Tj implies Pi > Pj
For the example, T1 has a higher priority than T2
This assignment is optimal for FPS
  if any process set can be scheduled (using pre-emptive priority-based scheduling) with a fixed-priority assignment scheme, then the given process set can also be scheduled with a rate monotonic assignment scheme

## Slide 24: RMS properties
Efficient Implementation
Overload condition will not cause problem
  A low priority task can not delay a hi-priority task
Many RTOS support RMS
Problems:
  Processor utilization is less than 1
    Sum of wcet/period for all the tasks
  Non optimal when periods and relative deadline differ
  Difficult to support aperiodic and sporadic tasks

## Slide 25: Example
Tasks Period ComputationTime Priority Utilization
p e P U=e/p
T1 4 1 3 0.25
T2 5 2 2 0.4
T3 20 5 1 0.25

## Slide 26: Gantt Chart for the example
T1
T2
T3
T1
T2
0
4
8
T3
T1
T1
T3
T2
12
T3
T2
16
T1
T2
20
T1

## Slide 27: Earliest Deadline First (EDF) Scheduling
The execution order is as per the order of absolute deadlines
At any time, the next task to run is the one with earliest deadline
  Note `any time’ – each time a new task is released, the priority is recomputed and possible preemption takes place
  Event-driven scheduling
Absolute deadlines are computed at run time from the relative deadlines
  and hence the scheme is dynamic
  Priorities are for task instance (jobs) rather than for tasks unlike in the case FPS

## Slide 28: Example
2
4
6
8
0
10
T1 (2, 0.9)
T2 (5, 2.3)
Pr(T2) is higher here
Notes: Is there a FPS for this? Answer is yes: RMA. Suppose you change tasks as: (2,1) and (5,2.5), then no RMA but EDF possible.

## Slide 29: Optimality of EDF
A set of tasks has a feasible schedule iff it has EDF schedule
  Under the assumption of preemption and no contention of resources
How to prove this result?
  Transform any feasible schedule into an EDF schedule

## Slide 30: Problems with EDF
Transient overload problem
  Some task may not complete in time which might cause some other task to miss its deadline
  A low priority may complete slowly and cause higher priority tasks to miss the deadline
  A domino effect can happen in which a no. of tasks miss their deadlines
Implementation is an issue
  It is dynamic and complex run-time system
  A queue of absolute deadlines need to be maintained throughout
  Either insertion or selection would be inefficient